## Slide 1
FINAL PROJECT STATUS
DeFT for 2.5D
Chiplet Networks
Noxim simulator extension, validated synthetic sweep, and claim-safe final report path.
128
routers modeled
64 chiplet + 64 interposer
16
physical VLs
startup permanent fault masks
2
VCs / VNs
VN.0 and VN.1 mapped to VC 0/1
Yusuf Tahir Orhan
CMP720 Final Project Presentation
May 2026
Main status
Implementation and validation infrastructure are complete enough for a descriptive final report. Stronger performance claims remain blocked until follow-up validation creates stronger artifacts.
Based on Extended Proposal requirements and the original DeFT paper

## Slide 2
PROPOSAL TO CURRENT STATUS
What changed after the proposal stage
02
Proposed
Implement DeFT in a cycle-accurate Noxim extension. Evaluate synthetic traffic and PARSEC/GEM5 traces. Compare against XY routing under VL fault scenarios. Report reachability, latency, and throughput.
Applied
Built DEFT_2_5D topology, physical VL fault model, two-VN transition enforcement, schema-v1 VL LUTs, DEFT route selection, synthetic traffic profiles, metrics export, runner, analysis, and final sweep.
Changed
PARSEC/GEM5 was deferred because the dependency and trace pipeline are absent. Standard XY is treated as a limited control baseline. Results are descriptive and blank-aware, not improvement claims.
Current recommendation: use the report as-is for tomorrow; revise later only after feedback or new validated artifacts.
CMP720 Final Project Presentation | DeFT 2.5D Noxim Extension

## Slide 3
PROBLEM DEFINITION
Inter-chiplet traffic has two coupled risks
03
Chiplet 0
Chiplet 1
Chiplet 2
Chiplet 3
Active interposer
VL
VL
>
>
Down to interposer
Up to chiplet
Deadlock risk
The up-down-up path can create cyclic channel dependencies even if each local chiplet mesh is deadlock-free.
Reliability risk
A failed Vertical Link removes physical access between a chiplet boundary router and the interposer.
CMP720 Final Project Presentation | DeFT 2.5D Noxim Extension

## Slide 4
IMPLEMENTED MODEL
The simulator now has a concrete 2.5D topology
04
4 x 4
mesh per chiplet
four chiplets total
8 x 8
active interposer
one mesh below chiplets
96
chiplet links
cardinal links inside chiplets
112
interposer links
cardinal interposer mesh
Component
Implemented value
Purpose
Router ID space
0..127
Separates chiplet routers from interposer routers
Packet endpoints
0..63
Synthetic traffic only injects at chiplet PEs
Vertical Links
16 physical bidirectional
Fault manager marks each VL functional or faulty
Fault policy
startup permanent
Fault mask is fixed before routing begins
Implemented model is traceable through docs/ARCHITECTURE.md and docs/DECISIONS.md

## Slide 5
VIRTUAL NETWORKS
Why VNs are needed: they break the dependency cycle
05
Without VN separation
chiplet H
Down
interposer H
Up
>
v
<
^
The same physical resource class can wait on itself around the up-down-up route.
With DeFT VNs
Rule 1
Routing from VN.1 to VN.0 is forbidden; VN.0 -> VN.1 is allowed.
Rule 2
In VN.0, Up-to-Horizontal movement is forbidden.
Rule 3
In VN.1, Horizontal-to-Down movement is forbidden.
Core idea: move through two ordered channel classes instead of one cyclic class.
This slide directly addresses the first-presentation feedback about virtual networks

## Slide 6
VIRTUAL NETWORKS
What the VNs do in the implementation
06
1. Assign VN
VN.0 maps to VC 0. VN.1 maps to VC 1. DeFT runs require exactly two VCs.
>
2. Route candidates
DEFT or topology-aware helpers propose legal physical directions.
>
3. Filter moves
VN.1 -> VN.0, Up-Horizontal in VN.0, and Horizontal-Down in VN.1 are rejected.
>
4. Reserve VC
The router reserves the selected output VC and forwards the flit with that VC state.
Why the area overhead exists
Hardware needs per-VC buffer/control resources, output-VC reservation logic, VN assignment/filter logic, and boundary-router LUT storage. The original DeFT paper reports less than 2% area overhead; this project discusses that as literature evidence, not synthesized silicon.
Why the overhead is limited
Only two VNs are used. The extra logic is concentrated around DeFT routing, transition checks, and boundary VL selection rather than replacing the whole router datapath.
Paper reference: DeFT hardware analysis reports <2% area overhead; no project synthesis was performed

## Slide 7
FAULT-AWARE ROUTING
DeFT separates permanent faults from runtime route choice
07
Startup fault manager
Applies a physical VL mask such as 0x0011 before packet routing.
>
Schema-v1 LUT
Keyed by fault mask, source chiplet, source router, and destination chiplet.
>
Selected VL pair
Chooses source exit and destination entry while avoiding marked faulty VLs.
Example lookup path
fault mask
source
destination
source exit
dest entry
0x0011
chiplet 0 / router 0
chiplet 3
functional VL
functional VL
Fail-closed behavior
Missing LUT entries or nonfunctional selected VLs return no legal output rather than silently inventing a path.
CMP720 Final Project Presentation | DeFT 2.5D Noxim Extension

## Slide 8
IMPLEMENTATION EVIDENCE
The deck can point to concrete code surfaces without showing raw code
08
Implementation surface
What it proves
Where it appears in the project
Topology + VL model
128-router DEFT_2_5D mapping and 16 physical VL inventory
DeftTopology.* and NoC construction
Fault injection
Startup permanent physical VL masks are validated before routing
DeftFaultInjectionManager.*
Virtual networks
VN.0/VN.1 assignment and illegal transition filtering are enforced
DeftVirtualNetwork.* and Router pipeline
DeFT route path
Runtime schema-v1 LUT selects source exit and destination entry
DeftVerticalLinkLut.* and Routing_DEFT.*
Experiment support
JSON metrics, runner manifests, and blank-aware analysis are reproducible
GlobalStats.* and experiment helpers
Presenter note: show this as implementation proof; do not spend time reading code in class.
Validation artifact
Status
Claim boundary
Final sweep
150/150 completed
descriptive finite-window evidence
Analysis cross-check
0 mismatches
tables match raw artifacts
CMP720 Final Project Presentation | DeFT 2.5D Noxim Extension

## Slide 9
REPORT TABLE 4 SUMMARY
Condition-level metrics show real measurements and blank-aware limits
09
150
completed runs
2 routings x 3 traffic x 5 masks x 5 seeds
30
condition cells
routing / traffic / mask groups
54
zero-injection runs
completed runs with no measured injection
0
raw mismatches
analysis cross-check passed
Condition-cell coverage
12 complete
13 partial
5 empty
Mode
Mask
Inj.
Recv.
Reach.
Lat.
Status
DEFT / local
0x0000
289
166
0.574
23.38
complete
DEFT / uniform
0x0001
137
84
0.613
23.96
complete
DEFT / hotspot
0x0011
114
72
0.632
40.36
partial
XY / local
0x0000
7
0
0.000
blank
partial
Interpretation: concrete results exist; ranking and improvement claims are still blocked.
Condensed from final report Table 4: Condition-Level Descriptive Metrics

## Slide 10
REPORT TABLE 5 SUMMARY
Pairwise readiness explains why the results are not a ranking claim
10
Traffic
Mask
XY
DEFT
Readiness
hotspot_3x10
0x0000
E
C
XY-empty
hotspot_3x10
0x0001
E
P
XY-empty
hotspot_3x10
0x0011
E
P
XY-empty
hotspot_3x10
0x0111
E
C
XY-empty
hotspot_3x10
0x1111
E
C
XY-empty
localized_40
all masks
P
C
latency-blank
uniform
0x0000-0x0111
P
C
latency-blank
uniform
0x1111
P
P
latency-blank
C / P / E
C = complete injection cell. P = partial injection cell. E = empty injection cell.
XY-empty
The XY side injected zero packets in the measured cell, so it cannot be compared.
latency-blank
Both modes may inject, but one side has no received packets, so latency ranking is blocked.
Condensed from final report Table 5: XY/DEFT Pairwise Readiness

## Slide 11
LIMITATIONS AND TRADE-OFFS
Current blockers are explicit, not hidden
11
Item
Current status
Why it matters
Blocked: PARSEC/GEM5 traces
No GEM5/PARSEC setup, traces, schema, or provenance
Cannot claim real-application workload support
Blocked: directional VL faults
Current fault model is physical bidirectional VL state
Paper-aligned single-direction fault cases need new design
Blocked: eventual delivery
Drain mode exists only as opt-in smoke-validated support
Needs a separate experiment before report claims
Comparison baseline
Standard XY is limited; IA-XY exists but limited results are exploratory
No ranking or latency-improvement claims yet
Embedded-system trade-off
DeFT buys reliability through extra VC resources, VN transition logic, and LUT storage. The project keeps this bounded to two VCs and documents the overhead as literature-based.
Scalability trade-off
More chiplets and fault states increase LUT generation and validation burden, so future work must version artifacts and avoid ad hoc trace imports.
CMP720 Final Project Presentation | DeFT 2.5D Noxim Extension

## Slide 12
CONCLUSION AND FUTURE WORK
The final message: implemented, validated, and honest about limits
12
Current status
A working DeFT-oriented Noxim extension exists with topology, routing, fault, VN, LUT, traffic, metric, runner, and analysis support. The final synthetic sweep completed and the final report package is ready.
Before final report submission
Do not rewrite the report tonight. After the presentation, update only if feedback or new validated artifacts justify it. Keep all unsupported claims out.
Future work
Versioned PARSEC/GEM5 trace schema, tiny trace fixtures, directional fault model, drain-based eventual-delivery experiments, stronger IA-XY baseline comparison, and RL-based VL selection.
Recommended answer if asked about final report: I would update it after feedback, but I would not strengthen results unless the new validation artifacts support the stronger wording.
End